Command / Outgoing request submitted from HyperTerminal				Reply / Incoming positive response returned by the / amplifier
P/T	Name	Arguments	Description	Arguments
P	CLREE	None or 1:[0]	Restore Default Settings / in non-volatile memory	None
P	FWRESET	None	Firmware reset	None
P	GETACCCURMAX	None	Get the maximum current setpoint in ACC mode. A zero value indicates no special limit in ACC mode than the one returned by / GETLDLIM	1: : Maximum Current in ACC mode, integer, mA
P	GETACTEFF / (For Laser with OutPwr Efficiency Protection.)	None	Get Actual Laser Efficiency values.	1: Actual Current, float, mA 2: Actual Power, float, mW / 3: Actual Efficiency, float, W/A
P	GETACTNOM / (For Laser with OutPwr Efficiency Protection.)	None	Get actual Nominal Laser / Current and Power used to calculate laser efficiency.	1: Current, float, mA / 2: Power, float, mW
P	GETAINUM	None	Get the number of analog / input signals	1: Number, integer
P	GETAISYM	1: Index, integer	Get the analog input symbol name that has the / given index	1: Symbol, string
P	GETAIVAL	1: Analog input / signal [0..6]	Get specified analog input / value	1: Value, float
P	GETALARM	1: Alarm case [0..4]	Get specified alarm state	1: Flag [0, 1]
P	GETALR	None	Get alarms	1: SHG Temperature, / flag [0, 1] / 2: TEC Temperature, / flag [0, 1] / 3: Pump Bias, flag[0,1] 4: Loss Of Output, / flag [0, 1] / 5:Case Temperature, flag[0,1]
P	GETALRLOG / Version 2.3.0.0 or later	1: Alarm case [0..4]	Get specified alarm accumulated elapsed time	1: # of Hours, integer [0..11930046] / 2: # of seconds, integer [0..3599]
P	GETCASELIM	1: LDD Board [1-3]	Get laser diode Case Temperature limit / parameters for the specified pump	1: Minimum Temperature, float °Celsius / 2: Maximum Temperature, float / °Celsius
P	GETCASETHR	None	Get laser diode Case Index and Case Temperature thresholds to generate alarm	1: LDD Board [1-3] / 2: Low Temperature, float / °Celsius / 3: High Temperature, float °Celsius
P	GETCHKEFF / (For Laser with OutPwr Efficiency Protection.)	1: Check Index: [0: Last Check, 1: Min Eff. Check]	Get Laser Efficiency values for the specified Check Index.	1: Current, float, mA 2: Power, float, mW / 3: Efficiency, float, W/A

Command / Outgoing request submitted from HyperTerminal				Reply / Incoming positive response returned by the / amplifier
P/T	Name	Arguments	Description	Arguments
P	GETCHKSTATE / (For Laser with OutPwr Efficiency Protection.)	None	Get Laser Efficiency ACTUAL Check State. / The State is OFF if the laser not running in APC. / The State is Low if actual current is below the Nominal Current. / The State is High if actual current is above the Nominal Current and laser Efficiency is being checked. / The State is Fault if the laser Efficiency has been below OutPwr Fault Threshold for a significant time and laser / has automatically shutdown.	1: State, integer [0:Off, 1:Low, 2: High, 3: Fault]
P	GETFAULT	1: Fault case [0..4] or / [0..5] (For Laser with OutPwr Efficiency Protection.)	Get specified fault	1: Flag [0, 1]
P	GETFLT	None	Get faults	1: SHG temperature, / flag [0, 1] / 2: Tec temperature, / flag [0, 1] / 3: Laser diode current, flag [0, 1] / 4: Watchdog timeout, / flag [0, 1] / 5: Case temperature, / flag [0, 1] / 6: OutPwr Efficiency, / flag [0, 1] / (For Laser with OutPwr Efficiency Protection.)
P	GETFLTLOG / Version 2.3.0.0 or later	1: Fault case [0..4] or / [0..5] (For Laser with OutPwr Efficiency Protection.)	Get specified fault accumulated latched counts	1: Fault Count, integer [0..65535]
P	GETFWREV	None	Get laser controller / firmware revision	1: Version, string
P	GETINPUT	11: Input index: [0: Interlock input, / 1: Hardware Bootload input, / Only for Key version : 2: Key OFF input	Get specified physical input actual state	1: Flag [0:Off, 1: On]
P	GETLASERSTATE	None	Get laser actual state	1: Laser State Code, integer
P	GETLASERSTATENUM	None	Get the number of laser / different states	1: Number, integer

Command / Outgoing request submitted from HyperTerminal				Reply / Incoming positive response returned by the / amplifier
P/T	Name	Arguments	Description	Arguments
P	GETLASERSTATESYM	1:Index, integer	Get the laser state code and symbol name for the specified index	1; Laser State Code, integer / 2: Laser State Symbol, string
P	GETLDCUR	1: LD pump [1-3]	Get specified laser diode / current set point when laser in manual mode	1: Current, integer, mA
P	GETLDENABLE	None	Get laser software enable / flag value	1: Flag [0: Disable, 1: / Enable]
P	GETLDLIM	1: LD pump [1-3]	Get laser diode limit parameters for the specified pump	1: Minimum Current, integer, mA / 2: Maximum Current, integer, mA / 3: Current Protection Threshold, integer,
P	GETLDMODE / Only for VFL MOPA	1: LD pump [1: Seed, 2:PreAmp, 3:Booster]	Get laser diode control mode when laser in automatic mode	1:Mode, integer,[ 0: ACC, 1: APC]
P	GETLDSTATE	1: LD pump [1-3]	Get the State for the / specified laser diode driver	1: State [0: Off, 1:On, 2: / Turning Off, 3:Turning On, 4: Fault]
P	GETLOOLIM	None	Get the Low and High power difference relative to the output power set point (In APC mode to / declare the LOS output Alarm	1: Low power, Float, dB 2: High Power Float, dB
P	GETLOOLIMPC	None	Get the Low and High power difference relative to the output power set point (In APC mode to / declare the LOS output Alarm	1: Low power, Float, % 2: High Power Float, %
P	GETMINEFFPC / (For Laser with OutPwr Efficiency Protection.)	None	Get Percent of Nominal / Laser Efficiency Minimum Threshold to generate OutPwr Efficiency Fault.	1: Percent of Nominal / Efficiency, integer, % [0..100]
P	GETMODEL	None	Get laser model number	1: Model, string
P	GETNOMCUR / (For Laser with OutPwr Efficiency Protection.)	None	Get BOL Nominal Laser Current used as a target to calculate laser efficiency.	1: Current, float, mA
P	GETNOMEFF / (For Laser with OutPwr Efficiency Protection.)	None	Get BOL Nominal Laser Efficiency used as a / Reference value to generate OutPwr Efficiency Fault.	1: Efficiency, float, W/A
P	GETOUT	None	Get outputs	1: Fault / flag [0, 1] / 2: Laser ON, / flag [0, 1] / 3: Laser Warming up and not ready to operate. / flag [0, 1] / 4: Service Affected, / flag [0, 1]
P	GETPOWER	1: 0	Get laser output power / set point in APC mode	1: Power, float, / mW

Command / Outgoing request submitted from HyperTerminal				Reply / Incoming positive response returned by the / amplifier
P/T	Name	Arguments	Description	Arguments
P	GETPOWERENABLE	None	Get laser mode	1:Mode, integer,[ 0: ACC, / 1: APC]
P	GETPOWERSETPTLIM	1: 0	Get limit parameters for the laser output power set point	1: Minimum Power, float, mW / 2: Maximum Power, float, mW
P	GETSHGCMD / Only for SHG Temp Tuning version	None	Get SHG actual / command	1: SHG Command [0: No / command executing, 1:SHG Tuning w/prerequisites initiated, 2: SHG Tuning aborting, 99: SHG Tuning w/out / prerequisites initiated ]
P	GETSHGTEMP	None	Get SHG sensor / temperature set point	1: Float, °Celsius
P	GETSHGTUNERDY	None	Get SHG Ready for Tuning state and left time	1: State [0: SHG Tuning w/prerequisites Not Ready, 1:SHG Tuning w/prerequisites Ready] / 2: # of Hours of laser operation left before next scheduled SHG Tuning, / 3: # of Seconds of laser operation left before end of warm-up at actual output power, integer, / [0..65535]
P	GETSHGTUNESTATE	None	Get SHG Tuning state and error status	1: State [0: Tuning OFF, 1:Tuning Completed, 2:Tuning Aborted, 3: Tuning In Progress] / 2:Error Status Bitmap [0..31] where: / 0: No Error, / 1: Laser not running in espected state, / 2: SHG Temp not set, 4: SHG Temp not stabilized, / 8: Output Power not stabilized in APC mode 16: SHG Temp out of limits] / 32: LD Current not stabilized in ACC mode, 64: No Power Peak / detected in ACC mode
P	GETSN	None	Get laser serial number	1: Serial #, string
P	GETSTATE	None	Get laser controller state	1: State, integer [0:Init, 1: / Normal, 2: ALS]
P	GETSTATUS	1: LDD Board [1-3]	Get the State for the specified laser diode driver board	1: LDD Alarms [0..511] / 2: LDD Faults [0..1023] / 3: LDD state [0:Init, 1:Normal, 2:ALS]

Command / Outgoing request submitted from HyperTerminal				Reply / Incoming positive response returned by the / amplifier
P/T	Name	Arguments	Description	Arguments
P	GETTECSETPT	1: TEC driver [1-3: TEC1- / 3, 4:SHG, 5:TEC5]	Get specified TEC driver / temperature set point	1: Temperature, Float, / °Celsius
P	GETTECSTATE	1: TEC driver [1-3: TEC1- / 3, 4:SHG, 5:TEC5]	Get the State for the specified TEC driver	1: State [0: Off, 1:On, 2: / Turning Off, 3:Turning On, 4: Fault]
P	GETTIMEOP	None	Get Time of Operation of laser head	1: # of Hours, integer [0..11930046] / 2: # of seconds, integer [0..3599] / 3: # of msec, integer [0.999]
P	GETTIMEOPCTRL	None	Get Time of Operation of / laser controller	1: # of Hours, integer / [0..11930046] / 2: # of seconds, integer [0..3599] / 3: # of msec, integer [0.999]
P	LASERSTATE / Only for VFL MOPA	1: Laser Stage [1: Seed, 2:PreAmp, 3:Booster]	Get specified laser stage actual state flag	1: Flag [0 : Output not OK / , 1 : Output OK]
P	LDCURRENT	1: LD pump [1-3]	Get specified laser diode / actual current	1: Current, integer, / mA
P	LDTEMP	1: LD pump [1: LD1]	Get specified laser diode / actual case temperature	1: Temperature, Float, / °Celsius
P	NOOPERATION	None	Do nothing .	None
P	POWER	1: Power INDEX / [0:Output, 1-3: LD1-3]	Get laser monitored powers	1: Power, float, mW
P	POWERENABLE	1:Mode, integer,[ 0: ACC, / 1: APC]	Set laser mode	None
P	RSTEFF / (For Laser with OutPwr Efficiency Protection.)	None	Reset Laser Efficiency Last and Min Eff. Check stats.	None
P	SAVEALL	None or 1:[0]	Save actual settings in / non-volatile memory	None
P	SETCASETHR	1: LDD Board [1-3] / 2: Low Temperature, float / °Celsius / 3: High Temperature, float °Celsius	Set laser diode Case Index and Case Temperature thresholds to generate alarm	None
P	SETLDCUR	1: LD pump [1-3] / 2: Current, integer, mA	Set specified laser diode current set point when / laser in manual mode	None
P	SETLDENABLE	1: Flag [0: Disable, 1: Enable]	Set laser software enable flag value	None
P	SETLOOLIM	1: Low power, Float, dB 2: High Power Float, dB	Set the Low and High power difference relative to the output power set point (In APC mode to declare the LOS output / Alarm	None

Command / Outgoing request submitted from HyperTerminal				Reply / Incoming positive response returned by the / amplifier
P/T	Name	Arguments	Description	Arguments
P	SETLOOLIMPC	1: Low power, Float, % 2: High Power Float, %	Set the Low and High power difference relative to the output power set point (In APC mode to declare the LOS output / Alarm	None
P	SETPOWER	1: 0 / 2: Power, float, mW	Set laser output power set point in APC mode	None
P	SETSHGCMD	1: SHG Command [1:Initiate SHG Tuning w/prerequisites, 2: Abort SHG Tuning, 99: Initiate / SHG Tuning w/out prerequisites]	Set SHG command	None
P	SETSHGTEMP	1: Float, °Celsius	Set SHG sensor / temperature set point	None
P	SHAI	None	Show analog input signals
P	SHALR	None	Show alarms
P	SHFAULT	None	Show faults
P	SHGTEMP	None	Get SHG sensor actual / temperature	1: Float, °Celsius
P	SHLASER	None	Show Laser settings and / measurements
P	TECCURRENT	1: TEC driver [1-3: TEC1- / 3, 4:SHG, 5:TEC5]	Get specified TEC driver / actual current	1: Current, integer, / mA
P	TECTEMP	1: TEC driver [1-3: TEC1- / 3, 4:SHG, 5:TEC5]	Get specified TEC sensor / actual temperature	1: Float, °Celsius
P	VCCMON	1: LD pump [1] / 2:VCC index[1:12Volt VCC, 2:5Volt VCC]	Get the specified VCC voltage	1: Voltage, float, Volt